## Slide 1
Impedance BC Implementation Comparison
Prior vs new IMPEDANCE implementation and IMPEDANCE vs RCR behavior
Scope
Solver code deltas in IMPEDANCE block setup and runtime behavior
Functionality: convolution controls, memory persistence, and validation
Rationale for major design decisions and tradeoffs
Implications for 3D-0D coupling and full 0D simulation modes
Evidence from fixtures and tests in svZeroDSolver/svZeroDTrees/svzt-agent
Comparison Axis A: Prior -> New IMPEDANCE
Period ownership moved to simulation_parameters.cardiac_period
Configure signature simplified; parser-level period requirement removed
Error handling now tied to model dt/period consistency at initialization
Comparison Axis B: IMPEDANCE vs RCR
History-based periodic convolution vs low-order lumped approximation
Persistent memory semantics under coupling retries and commits
Runtime cost/accuracy tradeoff via exact vs truncated kernel usage
Impedance BC implementation comparison: solver + workflow implications

## Slide 2
Architecture Context
Where IMPEDANCE behavior differs in full 0D and 3D-0D workflows
Full 0D Simulation Path
JSON boundary_conditions + simulation_parameters
Model::update_time() -> ImpedanceBC::update_time()
Convolution uses accepted one-cycle history
cardiac_period must align with dt and kernel length
Kernel history starts after one accepted period
Exact/truncated modes control per-step cost
3D-0D Coupled Iteration Path
Interface retry loop:
update_state() -> run_simulation() -> return_y()/return_ydot()
Committed persistent-state snapshot controls rollback-safe retries
Deterministic trial reruns from identical committed state
Commit occurs when caller accepts state via return_y/return_ydot
Behavior explicitly verified in interface test_04
Impedance BC implementation comparison: solver + workflow implications

## Slide 3
Solver Code Changes
Period ownership refactor and parser/configuration wiring updates
Prior implementation
Required period inside bc_values for each IMPEDANCE BC
Parser checked or set model.cardiac_cycle_period from BC field
configure(z, period, pd, mode, num_kernel_terms)
New implementation
period removed from IMPEDANCE bc_values contract
Single source of truth: simulation_parameters.cardiac_period
configure(z, pd, mode, num_kernel_terms)
Code-level evidence (HEAD commit 161870a5)
ImpedanceBC::configure signature - old: configure(const std::vector<double>& z, double period, double pd, ...) + new: configure(const std::vector<double>& z, double pd, ...) Initialization guard in ensure_initialized() const double period = model->cardiac_cycle_period; if (period <= 0.0) throw runtime_error(...cardiac_period > 0...); SimulationParameters::create_boundary_conditions period parsing and BC-level period consistency checks removed. IMPEDANCE now configures from z, Pd, convolution_mode, num_kernel_terms.
Impedance BC implementation comparison: solver + workflow implications

## Slide 4
Runtime Behavior of New IMPEDANCE BC
Discrete periodic convolution + one-cycle ring buffer memory
Implicit term z0*Q(n+1) is assembled in F; lagged terms accumulate into C
Lagged flows are read from accepted-state ring buffer (not transient trial state)
Startup rule: lagged convolution disabled until one full accepted period elapsed
Runtime checks enforce integer period/dt and z.size() == period steps
Execution modes
exact: num_kernel_terms = Np (full period)
truncated: user sets num_kernel_terms in [1, Np]
Per-step convolution cost scales with num_kernel_terms
Key invariants
dt must remain fixed after initialization
Persistent state compatibility checks include kernel size
Corrupted state payloads fail fast with explicit runtime errors
Impedance BC implementation comparison: solver + workflow implications

## Slide 5
Coupling Trial/Accept Semantics
Rollback safety for persistent memory in repeated external-coupling trials
return_y()/return_ydot() snapshots committed block persistent state
update_state() restores committed state before each new trial
run_simulation() advances from rollback-safe memory baseline
Evidence from tests
test_interface/test_04 repeats trial runs from same committed state
Asserts deterministic equivalence across repeated trials
Asserts observable state change after explicit commit
Confirms IMPEDANCE persistent memory participates in coupling protocol
Implication
3D solvers can probe multiple sub-iterations per external step without contaminating accepted impedance history.
Impedance BC implementation comparison: solver + workflow implications

## Slide 6
Functionality and Validation Surface
What the new implementation enables and how it is guarded
Capability / Guard | Behavior | Failure Mode / Message
Kernel modes | exact (full Np) and truncated (k <= Np) | Invalid mode or k out of range throws runtime_error
Period source | simulation_parameters.cardiac_period only | cardiac_period <= 0 rejected at initialization
Temporal consistency | Requires integer period/dt and fixed dt post-init | Non-integer ratio or dt change rejected
Kernel shape | z must be finite array with z.size() = Np | Missing/invalid/non-finite kernel rejected
Persistent state integrity | Supports get/set with compatibility checks | Corrupted payload or size mismatch rejected
Capability / Guard
Behavior
Failure Mode / Message
Compared with the prior contract, validation is centralized around model-level temporal consistency.
This removes duplicated period declarations and reduces mismatch states between BCs and global simulation settings.
Impedance BC implementation comparison: solver + workflow implications

## Slide 7
Implementation Decision Rationale
Why these design choices were made and what they trade off
Decision | Justification | Tradeoff
Remove BC-level period field | Single source of truth in simulation_parameters improves consistency and parser simplicity. | Requires users to set global cardiac_period explicitly for IMPEDANCE.
Initialize from model dt and cardiac_period | Runtime checks align kernel discretization with actual integration time-step. | Less tolerant to loosely specified inputs (fails fast by design).
Persistent state snapshot/restore in interface | Guarantees deterministic trial reruns for 3D coupling sub-iterations. | Adds interface bookkeeping for committed block states.
Exact + truncated convolution modes | Exposes accuracy/performance knob for large kernels and long periods. | Users must choose num_kernel_terms carefully for truncated mode.
Decision
Justification
Tradeoff
Impedance BC implementation comparison: solver + workflow implications

## Slide 8
IMPEDANCE vs RCR
Behavioral and practical comparison for model selection
Dimension | IMPEDANCE BC | RCR BC
Memory | One-cycle flow history ring buffer; explicit persistent state | Low-order internal states only; no long kernel memory
Frequency content | Directly encodes structured-tree kernel waveform | Approximates with 3-parameter lumped dynamics
Coupling retries | Designed for trial/accept rollback-safe semantics | Also retry-safe, but without long convolution history
Runtime cost | O(num_kernel_terms) per accepted step | Constant-time low-order update
Input contract | z kernel + global cardiac_period + mode | Rp, C, Rd parameters (+ optional variants)
Use cases | High-fidelity distal bed effects / wave reflections | Fast reduced-order approximation and robust baseline
Dimension
IMPEDANCE BC
RCR BC
Practical interpretation: IMPEDANCE provides richer distal dynamics at higher runtime/config complexity; RCR remains the lightweight baseline.
Impedance BC implementation comparison: solver + workflow implications

## Slide 9
3D-0D Workflow Implications
How the new impedance path behaves inside iterative tuning/submission loops
Tuning artifacts: optimized_params.csv, PA snapshot, tuned 0D coupling config
Gate outputs drive branch: converged -> postop submit, else regenerate reduced PA seed
Operational implications
Impedance tune_space is now validated end-to-end across defaults and patient overrides
Decision payloads explicitly include convergence state and regeneration path
3D submission logic can pause to needs_review on missing artifacts or failed extraction
Pipeline naturally separates physics tuning from scheduler lifecycle handling
Relevant modules
svzerodtrees.tuning.iteration
svzt-agent templates/slurm/job_template.sh
svzt config model/load merge rules
Impedance BC implementation comparison: solver + workflow implications

## Slide 10
Full 0D Implications
Configuration contract and reproducibility behavior after the refactor
Input contract update
// old (removed) "bc_values": { "period": 1.0, "Pd": 80000.0, "z": [...] } // new "simulation_parameters": { "cardiac_period": 1.0, ... } "bc_values": { "Pd": 80000.0, "z": [...], "convolution_mode": "exact" }
Cardiac period is globally defined and consumed by IMPEDANCE at initialization
Kernel length and period/dt mismatch now fail fast with explicit diagnostics
Fixture updates moved period declarations from BC block to simulation parameters
Reproducibility and debugging
Deterministic behavior depends on fixed dt and explicit committed-state transitions
Persistent state serialization includes dt, period steps, kernel terms, and flow history
Corrupted or incompatible persistent payloads trigger guarded runtime failures
Error messages now reference missing/invalid global cardiac_period rather than BC period
Recommended full-0D checklist
Set simulation_parameters.cardiac_period
Ensure period/dt is an integer count
Set z length to one period in time steps
Use truncated mode only with validated num_kernel_terms
Impedance BC implementation comparison: solver + workflow implications

## Slide 11
Evidence from Fixtures and Tests
Kernel and waveform evidence plus explicit test coverage
Kernel fixture evidence
Flow/pressure fixture evidence
Key tests and fixtures referenced
tests/cases/pulsatileFlow_R_impedance.json and result_pulsatileFlow_R_impedance.json
tests/test_interface/test_04 (coupling trial/accept deterministic semantics)
src/model/ImpedanceBC.{h,cpp} and src/solve/SimulationParameters.cpp
svzerodtrees/tuning/iteration.py and svzt-agent templates/slurm/job_template.sh
Takeaway: the refactor improves contract consistency and coupling safety while preserving a clear runtime cost/accuracy control surface.
Impedance BC implementation comparison: solver + workflow implications